## Slide 1
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training
WSQ Course Code: TGS-2025053922
Conducted by Tertiary Infotech Academy Pte Ltd · UEN: 201200696W
TSC: Quality Process Control · ELE-QUA-5006-1.1
Version v6 · 20 July 2026 · Trainer: Dr. Alfred Ang
© 2026 Tertiary Infotech Academy Pte Ltd. All rights reserved. · www.tertiarycourses.com.sg

## Slide 2
COURSE ADMINISTRATION
Welcome & Housekeeping
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
2

## Slide 3
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Mandatory)
1
Trainer displays the SSG digital attendance QR code
▶
2
Scan the QR code with your phone camera
▶
3
Key in your NRIC/FIN and submit
▶
4
Repeat for AM, PM and the assessment
▶
5
Keep 75% attendance to stay eligible for funding
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
3

## Slide 4
YOUR TRAINER · GENERAL
About the Trainer
Your Trainer
General Trainer template —
to be completed by the trainer
NAME
____________________________________________
TITLE / DESIGNATION
____________________________________________
QUALIFICATIONS
____________________________________________
AREAS OF EXPERTISE
____________________________________________
TRAINING & INDUSTRY EXPERIENCE
____________________________________________
CONTACT
____________________________________________
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
4

## Slide 5
YOUR TRAINER
About the Trainer
Dr. Alfred Ang
Principal Trainer
Tertiary Infotech Academy Pte. Ltd.
ROLE
Principal Trainer, Tertiary Infotech Academy Pte. Ltd.
QUALIFICATIONS
PhD; Certified Lean Six Sigma practitioner and trainer.
DELIVERS
WSQ courses on Lean Six Sigma, quality management and data analytics.
EXPERIENCE
Process improvement across manufacturing, service and technology sectors.
FOUNDER
Founder and lead instructor at Tertiary Infotech / Tertiary Courses.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
5

## Slide 6
ICE-BREAKER
Let's Know Each Other
• Your name, organisation and role.
• Your experience with process improvement or quality work (if any).
• One process at work that frustrates you — we may use it as your course scenario.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
6

## Slide 7
HOUSEKEEPING
Ground Rules
1
Set your mobile phone to silent mode.
2
Participate actively — no question is too small.
3
Mutual respect: agree to disagree.
4
One conversation at a time.
5
Be punctual; return from breaks on time.
6
75% attendance is required for certification.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
7

## Slide 8
COURSE PORTAL · lms-tms.tertiaryinfotech.com
Download Your Course Material
1
Go to lms-tms.tertiaryinfotech.com
▶
2
Sign in with the account details given in class
▶
3
Open this course from your dashboard
▶
4
Download the slides, Learner Guide and lab files
▶
5
Keep them open — the assessment is open book
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
8

## Slide 9
SCHEDULE · 9:30am-6:30pm with a 1-hour lunch
Lesson Plan — 2 Days, 8 Hours per Day
Day 1
Day 2
• Day 1 — Six Sigma foundations, Define phase and process mapping
– Digital attendance (AM) · Introductions
– Foundations: Quality, Lean, Six Sigma, belts, DMAIC
– Lab 1 — Yellow Belt role and scenario
– DEFINE: VOC, CTQ, charter, SIPOC, process mapping
– Labs 2-5 — VOC/waste, SIPOC, PDCA charter, DMAIC Define
• Day 2 — Measure, Analyse, Improve, Control and assessment
– Digital attendance (AM)
– MEASURE: wastes, data types, check sheets, DPMO
– Lab 6 — Data collection and KPIs
– ANALYZE: Pareto, run charts, 5 Whys, Fishbone
– Labs 7-8 — Data analysis and root cause
– IMPROVE & CONTROL: 5S, poka-yoke, control plan, A3
– Labs 9-10 · Revision · Final Assessment
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
9

## Slide 10
WSQ SKILLS FRAMEWORK
Skills Framework — TSC: Quality Process Control
• TSC Code: ELE-QUA-5006-1.1
• A1: Define project to meet process performance.
• A2: Establish project scope of work and the number of hours based on organisational requirements.
• A3: Analyse process performance data to identify root causes of variation.
• A4: Measure process performance against defined quality standards.
• A5: Recommend improvement and control actions to sustain process performance.
• K1: Lean and Six Sigma concepts, wastes, value and variation.
• K2: Quality tools and techniques for process improvement.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
10

## Slide 11
WHAT YOU'LL ACHIEVE
Learning Outcomes
1
LO1 — Define & scope
Define a project and establish scope using Define, Measure and Analyse.
2
LO2 — Lean & Six Sigma concepts
Apply value, waste, defects and variation to a work process.
3
LO3 — Map the process
Use SIPOC, process maps and value stream maps to expose handoffs.
4
LO4 — Measure & analyse
Use check sheets, Pareto, run charts and process metrics.
5
LO5 — Root cause
Identify root causes with 5 Whys, Fishbone and evidence.
6
LO6 — Improve & control
Recommend improvement and control actions that sustain the gain.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
11

## Slide 12
COURSE ROADMAP
Course Outline — We Follow DMAIC End to End
D
Define
• Foundations + Define
• VOC, CTQ, charter
• SIPOC, process maps
• Labs 1-5
M
Measure
• 8 wastes, data types
• Collection plan
• Yield, DPMO, sigma
• Lab 6
A
Analyze
• Variation
• Pareto, run charts
• 5 Whys, Fishbone
• Labs 7-8
I
Improve
• Solution selection
• 5S, poka-yoke
• Standard work
• Lab 9
C
Control
• Control plan
• Visual management
• A3 and handover
• Lab 10
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
12

## Slide 13
BEFORE YOU SIT THE ASSESSMENT
Briefing for Assessment
• Place phones and other materials under the table or on the floor.
• No photos or recording of assessment scripts.
• No discussion during the assessment.
• Use a black/blue pen for hard-copy assessments.
• No liquid paper / correction tape.
• Scripts are collected when time is up.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
13

## Slide 14
FINAL ASSESSMENT
Assessment
• Written Assessment (WA) — Short-Answer Questions (SAQ), 60 minutes, open book.
• Case Study (CS) — applied Lean Six Sigma tasks, 90 minutes, open book.
• Format: Open Book — slides, Learner Guide and approved materials only.
• A minimum of 75% attendance is required to be eligible for assessment and funding.
• An appeal process is available if required.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
14

## Slide 15
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey — scan the QR code on the LMS
▶
2
Assessment digital attendance — scan the SSG QR
▶
3
Sit the WA (SAQ), then the Case Study — open book
▶
4
Submit your answers on the LMS
▶
5
Sign the Assessment Summary Record
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
15

## Slide 16
FOUNDATIONS
Six Sigma Foundations
Quality · Lean · Six Sigma · Lean Six Sigma · Belt roles · The DMAIC roadmap
00
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
16

## Slide 17
FOUNDATIONS · QUALITY
What is Quality?
Before we can improve quality, we have to agree what the word actually means.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
17

## Slide 18
WHAT IS QUALITY?
Three Common Answers — and Why Only One Holds Up
Defect-free output
"Quality means zero defects"
• Necessary, but not sufficient.
• A product can be flawless and still not sell.
• Defect-free against WHOSE standard?
Meeting set standards
"Quality means meeting the spec"
• Better — it is measurable.
• But a spec can be set at the wrong level.
• Meeting a spec nobody wants is waste.
Meeting customer expectations
"Quality means the customer is satisfied"
• This is the Six Sigma definition.
• The customer sets the standard.
• Everything else follows from this.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
18

## Slide 19
FOUR KEY ACTIVITIES
Quality in a Nutshell
1
Understand requirements
Find out what the customer actually needs — in their own words.
2
Design to satisfy them
Build the product or service so it meets those requirements.
3
Deliver consistently
Reduce variation so every customer gets the same experience.
4
Improve continuously
Requirements move; the process has to keep up.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
19

## Slide 20
FOUNDATIONS · LEAN
What is Lean?
Lean maximises customer value by systematically removing everything the customer would not pay for.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
20

## Slide 21
WHAT IS LEAN?
Lean — The Core Idea
1
Origin
The Toyota Production System — refined in Japanese manufacturing from the 1950s.
2
Focus
Speed and flow: shorten the time from customer request to delivery.
3
Enemy
Waste (muda) — any effort that consumes resources but creates no customer value.
4
Method
See the process, find the waste, remove it, then standardise the improvement.
5
Applies to
Manufacturing AND service — hospitals, banks, IT service desks, government.
6
Yellow Belt use
Waste walks, process mapping, 5S and small Kaizen improvements.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
21

## Slide 22
LEAN · FIVE PRINCIPLES
The Five Lean Principles
1
Specify VALUE from the customer's point of view
▶
2
Map the VALUE STREAM and expose the waste in it
▶
3
Create FLOW so work moves without interruption
▶
4
Let the customer PULL work rather than pushing it
▶
5
Pursue PERFECTION through continuous improvement
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
22

## Slide 23
FOUNDATIONS · SIX SIGMA
What is Six Sigma?
A disciplined, data-driven method to reduce variation and defects — so the process delivers the same result every time.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
23

## Slide 24
WHAT IS SIX SIGMA?
Six Sigma — The Core Idea
1
Origin
Motorola, 1986 — later made famous by General Electric under Jack Welch.
2
Focus
Consistency: reduce the variation that creates defects.
3
Enemy
Variation — the spread that turns a good average into an unreliable experience.
4
Method
DMAIC, driven by data and statistics rather than opinion.
5
The target
No more than 3.4 defects per million opportunities (DPMO).
6
Yellow Belt use
Data collection, Pareto and run charts, root cause analysis.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
24

## Slide 25
THE STATISTICAL MEANING
Six Sigma as Standard Deviation
-3σ
-2σ
-1σ
μ
+1σ
+2σ
+3σ
LSL
USL
Sigma (σ) measures spread. The more sigmas that fit between the process mean and the specification limits, the less likely the process is to produce a defect.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
25

## Slide 26
WHY 'SIX' SIGMA
Sigma Level vs Defects per Million Opportunities
1σ
690,000 DPMO
31% yield
2σ
308,000 DPMO
69% yield
3σ
66,800 DPMO
93.3% yield
4σ
6,210 DPMO
99.38% yield
5σ
233 DPMO
99.977% yield
6σ
3.4 DPMO
99.99966% yield
Each sigma level is a step change, not an increment — moving 3σ → 4σ removes about 90% of the defects.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
26

## Slide 27
THE COST OF 'GOOD ENOUGH'
Why 99% Is Not Good Enough
99% quality
99.99966% quality
• At 99% quality (about 3.8σ)
– 20,000 lost articles of mail per hour
– Unsafe drinking water almost 15 minutes a day
– 5,000 incorrect surgical operations per week
– Two short or long landings at major airports daily
• At Six Sigma quality (3.4 DPMO)
– 7 lost articles of mail per hour
– Unsafe drinking water 1 minute every 7 months
– 1.7 incorrect surgical operations per week
– One short or long landing every 5 years
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
27

## Slide 28
THE COMBINED METHOD
Lean vs Six Sigma vs Lean Six Sigma
Lean
• Removes waste
• Improves speed and flow
• Question: is this step worth doing?
• Tools: VSM, 5S, Kaizen, poka-yoke
Six Sigma
• Reduces variation
• Improves consistency and accuracy
• Question: why does the result vary?
• Tools: DMAIC, Pareto, SPC, root cause
+
▼
Lean Six Sigma
Faster AND more consistent — remove the waste, then control the variation that remains.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
28

## Slide 29
HISTORY
A Short History of Lean Six Sigma
1950s
Toyota Production System — Lean is born
1986
Motorola coins Six Sigma
1995
GE adopts Six Sigma company-wide
2000s
Lean and Six Sigma merge
Today
Applied across service, healthcare, finance and IT
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
29

## Slide 30
THE CENTRAL EQUATION
Y = f(X)
The output Y is a function of the process inputs X. To change the result, change the inputs that drive it — not the result itself.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
30

## Slide 31
OUR COURSE SCENARIO
Y = f(X) in Practice — The Contoso Service Desk
1
Y — the output
Ticket assignment time, measured in hours from submission to assignment.
2
X — triage rules
How clearly the routing rules are written and understood.
3
X — staffing
How many agents are available at peak submission times.
4
X — ticket quality
How complete the information is when the ticket arrives.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
31

## Slide 32
WHO DOES WHAT
The Lean Six Sigma Belt Pathway
White Belt
Awareness of Six Sigma; supports local problem solving
Yellow Belt
Knows the basic tools; supports projects and runs small improvements
Green Belt
Leads smaller projects; assists Black Belts with analysis
Black Belt
Leads complex projects full time; coaches Green and Yellow Belts
Master Black Belt
Trains and mentors Belts; owns deployment strategy
This course certifies you at Yellow Belt — the level that supports projects and runs small improvements.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
32

## Slide 33
LSS YELLOW BELT
Your Role — the Lean Six Sigma Yellow Belt
1
Has basic knowledge
Understands the DMAIC roadmap and the 7 basic quality tools.
2
Supports the project
Contributes process knowledge as the subject-matter expert.
3
Collects the data
Runs check sheets and data collection under the project leader.
4
Maps the process
Builds SIPOC and process maps that expose handoffs and waste.
5
Runs small improvements
Leads Kaizen or PDCA improvements within their own work area.
6
Does not lead DMAIC
Larger, cross-functional DMAIC projects belong to a Green or Black Belt.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
33

## Slide 34
THE COURSE ROADMAP · WE FOLLOW THIS ORDER
The DMAIC Roadmap
D
Define
• Define the problem
• Capture VOC and CTQ
• Charter and scope
• Map with SIPOC
M
Measure
• Plan data collection
• Measure the baseline
• Calculate yield/DPMO
• Find the waste
A
Analyze
• Analyse the data
• Pareto and run charts
• 5 Whys and Fishbone
• Prove the root cause
I
Improve
• Generate solutions
• Select and pilot
• 5S and poka-yoke
• Standardise the work
C
Control
• Build the control plan
• Visual management
• Hand over to the owner
• Sustain the gain
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
34

## Slide 35
CHOOSING YOUR APPROACH
DMAIC vs PDCA — Which One Do I Use?
Small improvement
Full project
• PDCA — Plan, Do, Check, Act
– For small, local, fast improvements
– Days to a few weeks
– A Yellow Belt can run this
– Lower data requirement
– Used in Lab 4
• DMAIC — the full roadmap
– For larger, cross-functional problems
– Weeks to months
– Led by a Green or Black Belt
– Data and statistics required
– Supported by you from Lab 5 onward
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
35

## Slide 36
PDCA CYCLE
PDCA — The Small Improvement Cycle
1
PLAN — define the problem and plan the change
▶
2
DO — run the change at small scale
▶
3
CHECK — measure whether it actually worked
▶
4
ACT — adopt, adapt or abandon, then repeat
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
36

## Slide 37
PROJECT SELECTION
What Makes a Good Yellow Belt Project?
1
Related to your daily work
You know the process and can observe it directly.
2
Manageable in timeframe
Can be completed in weeks, not months.
3
Aligned to business goals
Someone in management cares about the result.
4
Data is available
You can measure the baseline and the improvement.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
37

## Slide 38
FOUNDATIONS · HANDS-ON
Yellow Belt Role, Certification Paths, and Improvement Scenario
LAB 1
Establish what a Lean Six Sigma Yellow Belt is accountable for, how the belt pathway progresses from White to Master Black Belt, and choose a small, manageable improvement scenario to carry through the whole course.
You'll build
A Yellow Belt responsibility table and a selected improvement scenario.
Tools & techniques: Belt role matrix, CSSC certification pathway, project selection criteria
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
38

## Slide 39
LAB 1 · Yellow Belt Role, Certification Paths,
Yellow Belt Role, Certification Paths, and Improvement Scenario
1
STEP 1 OF 5
Define the Yellow Belt role — list at least four responsibilities and your contribution to each.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
39

## Slide 40
LAB 1 · Yellow Belt Role, Certification Paths,
Yellow Belt Role, Certification Paths, and Improvement Scenario
2
STEP 2 OF 5
Compare the White, Yellow, Green, Black and Master Black Belt pathways in a table.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
40

## Slide 41
LAB 1 · Yellow Belt Role, Certification Paths,
Yellow Belt Role, Certification Paths, and Improvement Scenario
3
STEP 3 OF 5
Review the Contoso Service Desk scenario: tickets are slow to be assigned and status is unclear.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
41

## Slide 42
LAB 1 · Yellow Belt Role, Certification Paths,
Yellow Belt Role, Certification Paths, and Improvement Scenario
4
STEP 4 OF 5
Test your scenario against the 'good project' criteria — day-to-day work, manageable, aligned to business goals, data available.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
42

## Slide 43
LAB 1 · Yellow Belt Role, Certification Paths,
Yellow Belt Role, Certification Paths, and Improvement Scenario
5
STEP 5 OF 5
Record why a Yellow Belt supports rather than leads this improvement.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
43

## Slide 44
LAB 1 · VERIFY
Yellow Belt Role, Certification Paths, and Improvement Scenario
✅ Check your work
You can state the Yellow Belt role in one sentence and justify your scenario against all four selection criteria.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
44

## Slide 45
DMAIC · DEFINE
Define — Scope the Problem
VOC · CTQ · Project charter · Problem statement · Scope · SIPOC · Process mapping
D
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
45

## Slide 46
DEFINE · 25% OF THE COURSE
Key Concepts — Define
1
Voice of the Customer
Capture customer needs in their own words before deciding anything.
2
Critical to Quality
Translate each VOC need into a specific, measurable CTQ requirement.
3
Project charter
Problem statement, goal, scope, team and benefit — the project's contract.
4
Problem statement
Process, time period, measurable issue and impact — and never a solution.
5
SIPOC
The macro as-is map: Suppliers, Inputs, Process, Outputs, Customers.
6
Process mapping
Flowcharts and swimlanes expose the handoffs where delay and defects are born.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
46

## Slide 47
DMAIC · D — DEFINE
Define — What problem are we solving, and for whom?
The Define phase converts a vague complaint into a scoped, measurable problem statement everyone agrees on.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
47

## Slide 48
DEFINE · ROADMAP
Steps in the Define Phase
1
Capture the Voice of the Customer
▶
2
Translate VOC into CTQ requirements
▶
3
Write the problem and goal statements
▶
4
Charter and scope the project
▶
5
Map the process with SIPOC
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
48

## Slide 49
DEFINE · VOC
Voice of the Customer (VOC)
The needs and expectations of the customer, expressed in the customer's own language.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
49

## Slide 50
SOURCES OF VOC
Where VOC Comes From
1
Surveys
Structured and at scale, but limited to the questions you thought to ask.
2
Interviews
Rich and open-ended; best for understanding the 'why' behind a complaint.
3
Complaints & tickets
Already in your system — the cheapest and most honest VOC source.
4
Direct observation
Go and watch the work happen; customers cannot always articulate the problem.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
50

## Slide 51
THE CTQ TRANSLATION
VOC → Need → CTQ: The Translation
Voice of the Customer
Critical to Quality
• The customer says (VOC)
– "I don't want to wait too long"
– "I don't want cold pizza"
– "I never know where my ticket is"
– Vague, emotional, unmeasurable
• The measurable requirement (CTQ)
– Delivery in 30 minutes or less
– Pizza at 32°C minimum on arrival
– Status update within 4 working hours
– Specific, numeric, testable
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
51

## Slide 52
CTQ QUALITY CHECK
What Makes a Good CTQ?
1
Specific
Names exactly one characteristic of the output.
2
Measurable
Has a number and a unit you can actually record.
3
Linked to VOC
Traces back to something a customer genuinely said.
4
Has a target and limit
States the target value and the acceptable range around it.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
52

## Slide 53
DEFINE · THE PROJECT'S CONTRACT
The Project Charter
1
Business case
Why this project matters and what it is worth.
2
Problem statement
What is wrong, quantified, over a stated time period.
3
Goal statement
Metric, baseline, target and date.
4
Scope
What is in, and explicitly what is out.
5
Team and roles
Sponsor, project leader, Yellow Belt support and SMEs.
6
Milestones
The dates each DMAIC phase is expected to complete.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
53

## Slide 54
WRITING THE PROBLEM STATEMENT
Problem Statements — Good vs Bad
Avoid this
Aim for this
• Weak problem statement
– "The service desk is too slow."
– No process named
– No time period
– No measure or baseline
– No customer impact stated
– Hints at a solution ("we need more staff")
• Strong problem statement
– "Between 1 Jan and 31 Mar, tickets took an average of 9.4 working hours to be assigned against a 4-hour target, affecting 38% of employees and generating 210 chase-up contacts."
– Process, period, measure, baseline and impact — and no solution.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
54

## Slide 55
PROBLEM STATEMENT ANATOMY
The Four Components of a Problem Statement
1
What
The specific process and the defect or gap observed.
2
When
The time period the data covers.
3
How much
The measured baseline against the requirement.
4
So what
The impact on the customer and the business.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
55

## Slide 56
DEFINE · SIPOC
SIPOC — the macro 'as-is' map
One page that shows who supplies the process, what goes in, what happens, what comes out, and who receives it.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
56

## Slide 57
DEFINE · WORKED EXAMPLE
SIPOC — Contoso Service Desk Ticket Assignment
S — Suppliers
• Employees
• Line managers
• HR onboarding
• Monitoring tools
▶
I — Inputs
• Ticket form
• Category
• Priority
• Asset details
• Contact info
▶
P — Process
• 1. Ticket submitted
• 2. Auto-categorised
• 3. Triage review
• 4. Assigned to agent
• 5. Agent acknowledges
▶
O — Outputs
• Assigned ticket
• Assignment notification
• Priority classification
• SLA clock started
▶
C — Customers
• Employee
• Support agent
• Service desk manager
• IT leadership
Read left to right: suppliers provide the inputs, the process transforms them, and the outputs go to the customers.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
57

## Slide 58
SIPOC · METHOD
How to Build a SIPOC
1
Name the process and agree its start and stop points
▶
2
List the high-level steps — 5 to 7, no more
▶
3
Identify the outputs and who receives them
▶
4
Identify the inputs each step needs
▶
5
Identify who supplies each input
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
58

## Slide 59
DEFINE · PROCESS MAPPING
Why Process Maps Matter
1
Shows the real process
Not the process in the procedure manual — the one people actually follow.
2
Exposes handoffs
Delay and defects are usually created where work changes hands.
3
Builds shared understanding
The team often discovers they each believed a different process.
4
Finds the waste
Rework loops, waiting and duplicated approvals become visible.
5
Sets the baseline
You cannot improve a process you have not described.
6
Guides data collection
The map tells you where to put your measurement points.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
59

## Slide 60
CHOOSING THE RIGHT MAP
Three Levels of Process Map
SIPOC
Macro / 30,000 feet
• 5-7 steps on one page.
• Sets scope and boundaries.
• Built first, in the Define phase.
Process flowchart
Detailed / ground level
• Every step, decision and loop.
• Uses standard symbols.
• Reveals rework and delay.
Swimlane map
Detailed + ownership
• One lane per actor or team.
• Handoffs cross the lanes.
• Best for finding delay in handoffs.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
60

## Slide 61
READING A PROCESS MAP
Standard Process Map Symbols
1
Oval — Terminator
The start or the end of the process.
2
Rectangle — Process step
An activity or task being performed.
3
Diamond — Decision
A yes/no branch point in the flow.
4
Arrow — Flow
The direction work moves between steps.
5
Parallelogram — Data
An input to, or output from, a step.
6
D shape — Delay
Work waiting in a queue — usually where the waste is.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
61

## Slide 62
DEFINE · YOUR ONLINE TOOL
Your SIPOC & Process Map Builder
1
Where
alfredang.github.io/sipoc/ — no install, works in any browser.
2
Guided order
Enter Process → Outputs → Customers → Inputs → Suppliers, the way the method teaches.
3
Enforces the rules
Warns if you drift outside 5–7 steps, and tracks your pain-point count.
4
Tag pain points
Waiting, rework loop, unclear ownership, duplicate entry, missing decision rule.
5
Swimlane for free
Assign an actor to each step and the swimlane and handoff table build themselves.
6
Check my SIPOC
Validates the same rules your lab and assessment are marked against.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
62

## Slide 63
DEFINE · TOOL WALKTHROUGH
Using the SIPOC Builder in Lab 3
1
Set the process name, start point and stop point
▶
2
List the 5–7 process steps, then work outward to O, C, I, S
▶
3
Tag at least three pain points on the steps
▶
4
Assign an actor to each step — handoffs appear automatically
▶
5
Run 'Check my SIPOC', then export the PNG for your package
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
63

## Slide 64
WHAT YOU'LL DO
Hands-On Labs — Define
1
Lab 2 — Lean, Six Sigma, Waste, Voice of Customer, and
A VOC-to-CTQ translation table, a value-added analysis, and a waste wa
2
Lab 3 — SIPOC, Process Mapping, Handoffs, and SME Supp
A completed SIPOC and a detailed process map with pain points marked.
3
Lab 5 — DMAIC Overview, Problem Statement, Scope, and
A DMAIC phase table, refined problem statement, stakeholder map and be
4
Lab 4 (elective) — PDCA Small Improvement Project Charter
A one-page PDCA charter with problem statement, goal, scope and succes
5
Lab 11 (elective) — Affinity Diagram and Kano Analysis
An Affinity Diagram of clustered VOC themes and a Kano classification
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
64

## Slide 65
DMAIC · DEFINE · HANDS-ON
Lean, Six Sigma, Waste, Voice of Customer, and Value
LAB 2
Separate what the customer actually values from the waste that surrounds it. Capture the Voice of the Customer, translate it into measurable CTQ requirements, and run a waste walk using the eight wastes (DOWNTIME).
You'll build
A VOC-to-CTQ translation table, a value-added analysis, and a waste walk log.
Tools & techniques: VOC, CTQ tree, DOWNTIME eight wastes, value-added analysis
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
65

## Slide 66
LAB 2 · Lean, Six Sigma, Waste, Voice of Custo
Lean, Six Sigma, Waste, Voice of Customer, and Value
1
STEP 1 OF 6
Capture the Voice of the Customer — record at least five verbatim customer statements.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
66

## Slide 67
LAB 2 · Lean, Six Sigma, Waste, Voice of Custo
Lean, Six Sigma, Waste, Voice of Customer, and Value
2
STEP 2 OF 6
Translate each VOC statement into a need, then into a measurable CTQ requirement.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
67

## Slide 68
LAB 2 · Lean, Six Sigma, Waste, Voice of Custo
Lean, Six Sigma, Waste, Voice of Customer, and Value
3
STEP 3 OF 6
Classify each process activity as value-added, business-value-added or non-value-added.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
68

## Slide 69
LAB 2 · Lean, Six Sigma, Waste, Voice of Custo
Lean, Six Sigma, Waste, Voice of Customer, and Value
4
STEP 4 OF 6
Conduct a waste walk and tag each observation against the eight wastes (DOWNTIME).
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
69

## Slide 70
LAB 2 · Lean, Six Sigma, Waste, Voice of Custo
Lean, Six Sigma, Waste, Voice of Customer, and Value
5
STEP 5 OF 6
Distinguish a defect (output fails CTQ) from waste (effort the customer will not pay for).
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
70

## Slide 71
LAB 2 · Lean, Six Sigma, Waste, Voice of Custo
Lean, Six Sigma, Waste, Voice of Customer, and Value
6
STEP 6 OF 6
Identify which single waste type appears most often in your scenario.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
71

## Slide 72
LAB 2 · VERIFY
Lean, Six Sigma, Waste, Voice of Customer, and Value
✅ Check your work
Every CTQ is measurable with a target, and each waste observation is tagged to one of the eight waste types.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
72

## Slide 73
DMAIC · DEFINE · HANDS-ON
SIPOC, Process Mapping, Handoffs, and SME Support
LAB 3
Build the macro 'as-is' view with SIPOC, then drill into a detailed process map that shows every actor, system and handoff — the points where delay and defects are actually created.
You'll build
A completed SIPOC and a detailed process map with pain points marked.
Tools & techniques: SIPOC & Process Map Builder, process flowchart, swimlane map, standard process symbols
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
73

## Slide 74
LAB 3 · SIPOC, Process Mapping, Handoffs, and
SIPOC, Process Mapping, Handoffs, and SME Support
1
STEP 1 OF 6
Set the process boundaries — agree the explicit start and stop points first.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
74

## Slide 75
LAB 3 · SIPOC, Process Mapping, Handoffs, and
SIPOC, Process Mapping, Handoffs, and SME Support
2
STEP 2 OF 6
Build the SIPOC with the online builder: Suppliers, Inputs, Process (5-7 high-level steps), Outputs, Customers.
https://alfredang.github.io/sipoc/
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
75

## Slide 76
LAB 3 · SIPOC, Process Mapping, Handoffs, and
SIPOC, Process Mapping, Handoffs, and SME Support
3
STEP 3 OF 6
Expand into a detailed process map: Step, Actor, Activity, System, Handoff.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
76

## Slide 77
LAB 3 · SIPOC, Process Mapping, Handoffs, and
SIPOC, Process Mapping, Handoffs, and SME Support
4
STEP 4 OF 6
Assign an actor to each step — the tool generates the swimlane and detects every handoff for you.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
77

## Slide 78
LAB 3 · SIPOC, Process Mapping, Handoffs, and
SIPOC, Process Mapping, Handoffs, and SME Support
5
STEP 5 OF 6
Tag pain points on the steps — waiting, rework loop, unclear ownership, duplicate entry or missing decision rule (at least three).
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
78

## Slide 79
LAB 3 · SIPOC, Process Mapping, Handoffs, and
SIPOC, Process Mapping, Handoffs, and SME Support
6
STEP 6 OF 6
Prepare SME notes for the Green Belt: what you observed and what needs validation.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
79

## Slide 80
LAB 3 · VERIFY
SIPOC, Process Mapping, Handoffs, and SME Support
✅ Check your work
Run 'Check my SIPOC' in the tool — all five columns populated, 5-7 steps, at least three pain points, and every handoff owned on both sides.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
80

## Slide 81
DMAIC · DEFINE · HANDS-ON
Elective — PDCA Small Improvement Project Charter
LAB 4
ELECTIVE
Not every improvement needs a full DMAIC project. Use PDCA to charter a small, fast improvement that a Yellow Belt can run under guidance — with a problem statement, a measurable goal and a defined check point.
You'll build
A one-page PDCA charter with problem statement, goal, scope and success measure.
Tools & techniques: PDCA cycle, problem/goal statements, scope in-out, stakeholder list
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
81

## Slide 82
LAB 4 · Elective — PDCA Small Improvement Proj
Elective — PDCA Small Improvement Project Charter
1
STEP 1 OF 6
Map the four PDCA phases to concrete actions for your scenario.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
82

## Slide 83
LAB 4 · Elective — PDCA Small Improvement Proj
Elective — PDCA Small Improvement Project Charter
2
STEP 2 OF 6
Write the problem statement: process, time period, measurable issue and impact — no solution.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
83

## Slide 84
LAB 4 · Elective — PDCA Small Improvement Proj
Elective — PDCA Small Improvement Project Charter
3
STEP 3 OF 6
Write a measurable goal statement: metric, baseline, target and date.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
84

## Slide 85
LAB 4 · Elective — PDCA Small Improvement Proj
Elective — PDCA Small Improvement Project Charter
4
STEP 4 OF 6
Define scope with an explicit in-scope / out-of-scope table to prevent scope creep.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
85

## Slide 86
LAB 4 · Elective — PDCA Small Improvement Proj
Elective — PDCA Small Improvement Project Charter
5
STEP 5 OF 6
Identify stakeholders and the decision you will make after the Check phase.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
86

## Slide 87
LAB 4 · Elective — PDCA Small Improvement Proj
Elective — PDCA Small Improvement Project Charter
6
STEP 6 OF 6
Confirm the improvement is small enough to test within two weeks.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
87

## Slide 88
LAB 4 · VERIFY
Elective — PDCA Small Improvement Project Charter
✅ Check your work
Your goal statement contains a metric, a baseline, a target and a date, and your problem statement names no solution.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
88

## Slide 89
DMAIC · DEFINE · HANDS-ON
DMAIC Overview, Problem Statement, Scope, and Stakeholders
LAB 5
Step up from PDCA to the full DMAIC roadmap. Clarify what each phase delivers, where a Yellow Belt contributes most, and prepare defensible Define-phase information for the project leader.
You'll build
A DMAIC phase table, refined problem statement, stakeholder map and benefit estimate.
Tools & techniques: DMAIC roadmap, project charter, stakeholder analysis, CTQ linkage
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
89

## Slide 90
LAB 5 · DMAIC Overview, Problem Statement, Sco
DMAIC Overview, Problem Statement, Scope, and Stakeholders
1
STEP 1 OF 6
Summarise all five DMAIC phases: purpose, key deliverable and Yellow Belt support role.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
90

## Slide 91
LAB 5 · DMAIC Overview, Problem Statement, Sco
DMAIC Overview, Problem Statement, Scope, and Stakeholders
2
STEP 2 OF 6
Refine the problem statement so it is specific, measurable and solution-free.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
91

## Slide 92
LAB 5 · DMAIC Overview, Problem Statement, Sco
DMAIC Overview, Problem Statement, Scope, and Stakeholders
3
STEP 3 OF 6
Identify stakeholders and classify each by influence and interest.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
92

## Slide 93
LAB 5 · DMAIC Overview, Problem Statement, Sco
DMAIC Overview, Problem Statement, Scope, and Stakeholders
4
STEP 4 OF 6
Define the project scope and state the expected benefit in business terms.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
93

## Slide 94
LAB 5 · DMAIC Overview, Problem Statement, Sco
DMAIC Overview, Problem Statement, Scope, and Stakeholders
5
STEP 5 OF 6
Link the problem back to the CTQ requirements captured in Lab 2.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
94

## Slide 95
LAB 5 · DMAIC Overview, Problem Statement, Sco
DMAIC Overview, Problem Statement, Scope, and Stakeholders
6
STEP 6 OF 6
Confirm which DMAIC phases a Yellow Belt can support most strongly.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
95

## Slide 96
LAB 5 · VERIFY
DMAIC Overview, Problem Statement, Scope, and Stakeholders
✅ Check your work
Your problem statement passes the 'no solution named' test and every stakeholder has a defined engagement approach.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
96

## Slide 97
DMAIC · DEFINE · HANDS-ON
Elective — Affinity Diagram and Kano Analysis
LAB 11
ELECTIVE
Two Define-phase tools from the original course. Use an Affinity Diagram to cluster unstructured VOC input into themes, then apply Kano Analysis to classify requirements as Must-Be, One-Dimensional or Delighter.
You'll build
An Affinity Diagram of clustered VOC themes and a Kano classification table.
Tools & techniques: Affinity Diagram, Kano Analysis, VOC clustering
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
97

## Slide 98
LAB 11 · Elective — Affinity Diagram and Kano A
Elective — Affinity Diagram and Kano Analysis
1
STEP 1 OF 4
Write each VOC statement on a separate note — one idea per note.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
98

## Slide 99
LAB 11 · Elective — Affinity Diagram and Kano A
Elective — Affinity Diagram and Kano Analysis
2
STEP 2 OF 4
Cluster related notes into natural groups without talking, then name each group.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
99

## Slide 100
LAB 11 · Elective — Affinity Diagram and Kano A
Elective — Affinity Diagram and Kano Analysis
3
STEP 3 OF 4
Classify each requirement as Must-Be, One-Dimensional or Delighter.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
100

## Slide 101
LAB 11 · Elective — Affinity Diagram and Kano A
Elective — Affinity Diagram and Kano Analysis
4
STEP 4 OF 4
Plot the requirements on the Kano diagram and identify where to invest first.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
101

## Slide 102
LAB 11 · VERIFY
Elective — Affinity Diagram and Kano Analysis
✅ Check your work
Every VOC note sits in exactly one named affinity group and carries a Kano classification.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
102

## Slide 103
PHASE RECAP
Recap — Define
• Voice of the Customer — Capture customer needs in their own words before deciding anything.
• Critical to Quality — Translate each VOC need into a specific, measurable CTQ requirement.
• Project charter — Problem statement, goal, scope, team and benefit — the project's contract.
• Problem statement — Process, time period, measurable issue and impact — and never a solution.
• SIPOC — The macro as-is map: Suppliers, Inputs, Process, Outputs, Customers.
• Process mapping — Flowcharts and swimlanes expose the handoffs where delay and defects are born.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
103

## Slide 104
DMAIC · MEASURE
Measure — Quantify Performance
The 8 wastes · Data types · Data collection plan · Check sheets · Yield · DPMO · Sigma level
M
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
104

## Slide 105
MEASURE · 25% OF THE COURSE
Key Concepts — Measure
1
The 8 wastes
DOWNTIME — Defects, Overproduction, Waiting, Non-utilised talent, Transport, Inventory, Motion, Extra-processing.
2
Types of data
Continuous vs discrete; nominal vs ordinal — the data type drives the tool choice.
3
Data collection plan
What, who, when and how — with operational definitions to remove ambiguity.
4
Check sheets
A simple structured form is the most reliable way to capture process data.
5
Process metrics
Yield, DPU, DPO and DPMO quantify how well the process actually performs.
6
Sigma level
Convert DPMO into a sigma level to benchmark the process against Six Sigma.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
105

## Slide 106
DMAIC · M — MEASURE
Measure — How big is the problem, really?
The Measure phase replaces opinion with a trustworthy baseline you can improve against.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
106

## Slide 107
MEASURE · ROADMAP
Steps in the Measure Phase
1
Identify the waste in the current process
▶
2
Decide what to measure and define it precisely
▶
3
Build the data collection plan and check sheet
▶
4
Collect the baseline data
▶
5
Calculate yield, DPMO and sigma level
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
107

## Slide 108
MEASURE · WASTE (MUDA)
What is Waste?
Anything beyond the minimum information, equipment, material and effort absolutely required to add value for the customer.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
108

## Slide 109
MEASURE · THE 8 WASTES
The Eight Wastes of Lean — DOWNTIME
DOWNTIME
8 wastes
D
Defects
O
Overproduction
W
Waiting
N
Non-utilised talent
T
Transport
I
Inventory
M
Motion
E
Extra-processing
Waste is any effort the customer would not willingly pay for.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
109

## Slide 110
DOWNTIME IN PRACTICE
The Eight Wastes in a Service Process
1
D — Defects
Wrong ticket category, incomplete information, work that must be redone.
2
O — Overproduction
Reports nobody reads; producing output before it is needed.
3
W — Waiting
Tickets sitting in a queue waiting for triage or approval.
4
N — Non-utilised talent
Skilled agents doing routine data entry a form could handle.
5
T — Transport
Tickets bouncing between teams before reaching the right owner.
6
I — Inventory
A growing backlog of unassigned tickets.
7
M — Motion
Switching between four systems to resolve one ticket.
8
E — Extra-processing
Approvals and checks that add no value to the customer.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
110

## Slide 111
MEASURE · VALUE ANALYSIS
Value-Added vs Non-Value-Added
Value-added (VA)
The customer would pay for it
• Changes the product or service.
• Done right the first time.
• The customer cares that it happened.
• Example: diagnosing the actual fault.
Business-value-added (BVA)
Required, but not by the customer
• Needed for legal or regulatory reasons.
• Required to run the business.
• Minimise it — you cannot remove it.
• Example: mandatory audit logging.
Non-value-added (NVA)
Pure waste — remove it
• Consumes time and resource for nothing.
• The customer would never pay for it.
• Attack this first.
• Example: a ticket waiting in a queue.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
111

## Slide 112
AN IMPORTANT DISTINCTION
Waste is not the same as a defect.
A defect is an output that fails the CTQ requirement. Waste is any effort along the way that the customer would not willingly pay for. Every defect creates waste — but most waste is not a defect.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
112

## Slide 113
MEASURE · DATA TYPES
Types of Data — and Why It Matters
Continuous data
Measured on a scale
• Any value within a range.
• Time, cost, temperature, length.
• More information per data point.
• Needs a smaller sample size.
Discrete / attribute data
Counted in whole units
• Counts and categories only.
• Number of defects, pass/fail.
• Less information per data point.
• Needs a much larger sample.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
113

## Slide 114
THE FOUR MEASUREMENT SCALES
Nominal, Ordinal, Interval, Ratio
1
Nominal
Labels with no order — ticket category, agent name, department.
2
Ordinal
Ordered categories, but the gaps are not equal — priority P1/P2/P3, satisfaction 1-5.
3
Interval
Equal gaps, but no true zero — temperature in °C, calendar dates.
4
Ratio
Equal gaps and a true zero — assignment time, cost, number of tickets.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
114

## Slide 115
WHY THIS MATTERS
The data type decides the tool.
Choose your chart, your test and your sample size AFTER you know what kind of data you are holding — not before.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
115

## Slide 116
MEASURE · PLANNING THE DATA
The Data Collection Plan
1
What
Which metric, and what exactly counts as one observation.
2
Why
Which CTQ or problem statement this metric supports.
3
How
Automated report preferred; manual capture only when unavoidable.
4
Who
Someone who knows the process and is available to do it consistently.
5
When
The frequency and the exact period the data covers.
6
How many
The sample size — enough to be representative, not so many it is unaffordable.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
116

## Slide 117
MEASURE · OPERATIONAL DEFINITIONS
Operational definitions remove the argument.
"Assignment time" means nothing until you state it precisely: the elapsed working hours from ticket submission timestamp to the first agent assignment timestamp, excluding weekends and public holidays.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
117

## Slide 118
MEASURE · CHECK SHEETS
Check Sheets — the Simplest Reliable Tool
1
One row per observation
Never summarise as you collect — record the raw event.
2
Pre-printed categories
Tick a box rather than writing free text; free text cannot be counted.
3
Mutually exclusive
Every observation must fall into exactly one category.
4
Include the context
Date, time, shift and who recorded it — you will need this later.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
118

## Slide 119
MEASURE · SAMPLING
Sampling Techniques
1
Simple random
Every unit has an equal chance of being selected.
2
Stratified random
Split the population into groups, then sample randomly within each group.
3
Systematic
Take every nth unit — simple, but beware of hidden cycles in the data.
4
Cluster
Sample whole naturally occurring groups when individual sampling is impractical.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
119

## Slide 120
MEASURE · THE STANDARD METRICS
Process Performance Metrics
Yield
Yield = (Good units / Total units) × 100
950 of 1,000 tickets assigned on time → 95% yield
DPU
DPU = Defects / Units
600 defects across 1,000 tickets → DPU = 0.6
DPO
DPO = Defects / (Units × Opportunities)
600 defects, 1,000 tickets, 3 opportunities each → DPO = 0.2
DPMO
DPMO = DPO × 1,000,000
DPO of 0.2 → 200,000 DPMO
An 'opportunity' is any single chance for a defect to occur on one unit — agree the count before you measure.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
120

## Slide 121
MEASURE · YIELD
Yield — Three Different Questions
1
Classic yield
What fraction of units passed final inspection? Ignores any rework along the way.
2
First pass yield (FPY)
What fraction passed with NO rework at any step? The honest number.
3
Rolled throughput yield (RTY)
Multiply the FPY of every step — the probability a unit passes cleanly through the entire process.
4
Why RTY matters
Five steps at 95% each give an RTY of only 77% — small defect rates compound fast.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
121

## Slide 122
MEASURE · SIGMA LEVEL
From DPMO to Sigma Level
Sigma level
Look DPMO up in the sigma conversion table
200,000 DPMO ≈ 2.3σ
Our example
Yield 99.5% → 5,000 DPMO
5,000 DPMO ≈ 4.1σ
The Six Sigma target
3.4 DPMO
99.99966% yield
Sigma level is the common yardstick that lets you compare performance across completely different processes.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
122

## Slide 123
MEASURE · THE BUSINESS CASE
Cost of Poor Quality (COPQ)
1
Internal failure
Defects found before the customer sees them — rework, scrap, re-triage.
2
External failure
Defects the customer finds — complaints, escalations, lost trust.
3
Appraisal cost
The cost of inspecting and checking for defects.
4
Prevention cost
The cost of stopping defects happening — training, poka-yoke, better design.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
123

## Slide 124
WHAT YOU'LL DO
Hands-On Labs — Measure
1
Lab 6 — Data Collection, KPIs, Check Sheets, and Basic
A data collection plan, an operational definition set and a working ch
2
Lab 12 (elective) — Value Stream Map and Takt Time
A value stream map with lead time, process time and a calculated takt
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
124

## Slide 125
DMAIC · MEASURE · HANDS-ON
Data Collection, KPIs, Check Sheets, and Basic Metrics
LAB 6
Replace anecdote with evidence. Define KPIs with unambiguous operational definitions, design a check sheet, plan the sampling approach, and understand which data type you are collecting — because the data type drives the tool.
You'll build
A data collection plan, an operational definition set and a working check sheet.
Tools & techniques: KPI definition, operational definitions, check sheets, sampling, data types
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
125

## Slide 126
LAB 6 · Data Collection, KPIs, Check Sheets, a
Data Collection, KPIs, Check Sheets, and Basic Metrics
1
STEP 1 OF 6
Classify your data: continuous vs discrete, nominal vs ordinal — and why it matters.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
126

## Slide 127
LAB 6 · Data Collection, KPIs, Check Sheets, a
Data Collection, KPIs, Check Sheets, and Basic Metrics
2
STEP 2 OF 6
Define KPIs with operational definitions, data source and collection frequency.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
127

## Slide 128
LAB 6 · Data Collection, KPIs, Check Sheets, a
Data Collection, KPIs, Check Sheets, and Basic Metrics
3
STEP 3 OF 6
Design a check sheet capturing date, ticket ID, type, assignment time and defect category.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
128

## Slide 129
LAB 6 · Data Collection, KPIs, Check Sheets, a
Data Collection, KPIs, Check Sheets, and Basic Metrics
4
STEP 4 OF 6
Define mutually exclusive defect categories so every observation lands in exactly one.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
129

## Slide 130
LAB 6 · Data Collection, KPIs, Check Sheets, a
Data Collection, KPIs, Check Sheets, and Basic Metrics
5
STEP 5 OF 6
Plan sampling: how many, how often, by whom — and identify possible bias.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
130

## Slide 131
LAB 6 · Data Collection, KPIs, Check Sheets, a
Data Collection, KPIs, Check Sheets, and Basic Metrics
6
STEP 6 OF 6
State which KPI best reflects the customer pain point from your VOC work.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
131

## Slide 132
LAB 6 · VERIFY
Data Collection, KPIs, Check Sheets, and Basic Metrics
✅ Check your work
Two different people reading your operational definition would record the same value for the same event.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
132

## Slide 133
DMAIC · MEASURE · HANDS-ON
Elective — Value Stream Map and Takt Time
LAB 12
ELECTIVE
Extend process mapping into Lean metrics. Map the value stream with process and wait times, calculate process cycle efficiency, then compute takt time to see whether the process can meet customer demand.
You'll build
A value stream map with lead time, process time and a calculated takt time.
Tools & techniques: SIPOC & Process Map Builder, value stream mapping, lead time, WIP, takt time
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
133

## Slide 134
LAB 12 · Elective — Value Stream Map and Takt T
Elective — Value Stream Map and Takt Time
1
STEP 1 OF 4
Map the value stream: each step with its process time and the wait time between steps. Start from your Lab 3 process map.
https://alfredang.github.io/sipoc/
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
134

## Slide 135
LAB 12 · Elective — Value Stream Map and Takt T
Elective — Value Stream Map and Takt Time
2
STEP 2 OF 4
Total the value-added time and the lead time, then compute process cycle efficiency.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
135

## Slide 136
LAB 12 · Elective — Value Stream Map and Takt T
Elective — Value Stream Map and Takt Time
3
STEP 3 OF 4
Calculate takt time = available working time / customer demand.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
136

## Slide 137
LAB 12 · Elective — Value Stream Map and Takt T
Elective — Value Stream Map and Takt Time
4
STEP 4 OF 4
Compare cycle time against takt time to identify the bottleneck step.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
137

## Slide 138
LAB 12 · VERIFY
Elective — Value Stream Map and Takt Time
✅ Check your work
Your lead time equals the sum of all process and wait times, and takt time is expressed per unit.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
138

## Slide 139
PHASE RECAP
Recap — Measure
• The 8 wastes — DOWNTIME — Defects, Overproduction, Waiting, Non-utilised talent, Transport, Inventory, Motion, Extra-processing.
• Types of data — Continuous vs discrete; nominal vs ordinal — the data type drives the tool choice.
• Data collection plan — What, who, when and how — with operational definitions to remove ambiguity.
• Check sheets — A simple structured form is the most reliable way to capture process data.
• Process metrics — Yield, DPU, DPO and DPMO quantify how well the process actually performs.
• Sigma level — Convert DPMO into a sigma level to benchmark the process against Six Sigma.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
139

## Slide 140
DMAIC · ANALYZE
Analyze — Find the Root Cause
Variation · Pareto · Run charts · 5 Whys · Fishbone · Multi-voting · Evidence
A
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
140

## Slide 141
ANALYZE · 20% OF THE COURSE
Key Concepts — Analyze
1
Variation
Common cause is built into the process; special cause is an external, assignable signal.
2
Pareto analysis
The 80/20 rule separates the vital few causes from the trivial many.
3
Run charts
Plot the metric over time to reveal trend, shift, cluster and oscillation.
4
5 Whys
Ask why repeatedly to drill from the symptom down to an actionable cause.
5
Fishbone diagram
Organise candidate causes by category — Manpower, Method, Machine, Material, Measurement.
6
Evidence testing
A cause is only a root cause when the data you collected supports it.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
141

## Slide 142
DMAIC · A — ANALYZE
Analyze — Why is this happening?
The Analyze phase moves the team from a measured symptom to a proven, actionable root cause.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
142

## Slide 143
ANALYZE · ROADMAP
Steps in the Analyze Phase
1
Study the data and the process map
▶
2
Generate a list of potential causes (Xs)
▶
3
Organise the causes with a Fishbone diagram
▶
4
Drill down with the 5 Whys
▶
5
Test each candidate cause against the evidence
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
143

## Slide 144
ANALYZE · UNDERSTANDING VARIATION
Two Kinds of Variation — and Two Different Responses
Common cause
Built into the process
• Always present, random, predictable range.
• The process is stable but imperfect.
• Response: change the PROCESS.
• Reacting to individual points makes it worse.
Special cause
An external, assignable signal
• Unusual, traceable to a specific event.
• Something changed that should not have.
• Response: investigate THAT event.
• Fix the cause, then remove it for good.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
144

## Slide 145
THE MOST COMMON ANALYSIS MISTAKE
Do not react to a single data point.
Treating common-cause variation as if it were special cause — called tampering — reliably makes the process worse, not better.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
145

## Slide 146
ANALYZE · PARETO
The Pareto Principle — the 80/20 rule
Roughly 80% of the effects come from 20% of the causes. Find that 20% and you get most of the improvement for a fraction of the effort.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
146

## Slide 147
ANALYZE · WORKED EXAMPLE
Pareto Chart — Causes of Delayed Ticket Assignment
210
Unclear
triage rules
155
Peak-hour
understaffing
95
Incomplete
ticket info
48
System
slowness
30
Wrong
category
12
Other
38%
66%
84%
92%
98%
100%
80%
Two categories — unclear triage rules and peak-hour understaffing — account for about 66% of all delays. Start there.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
147

## Slide 148
PARETO · METHOD
How to Build a Pareto Chart
1
Agree the categories and make them mutually exclusive
▶
2
Count the occurrences in each category
▶
3
Sort the categories in descending order
▶
4
Calculate the cumulative percentage
▶
5
Plot bars plus the cumulative line and read off the vital few
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
148

## Slide 149
ANALYZE · SEEING BEHAVIOUR OVER TIME
Run Chart — Average Ticket Assignment Time by Day
Median 9.5
D1
D2
D3
D4
D5
D6
D7
D8
D9
D10
A single point above the median is normal variation. A run of 7+ points on one side signals a real shift.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
149

## Slide 150
ANALYZE · RUN CHART RULES
Reading a Run Chart — Five Patterns
1
Trend
7 or more consecutive points rising or falling — the process is drifting.
2
Shift
8 or more consecutive points on one side of the median — something changed.
3
Cluster
Points grouped together — suggests a periodic or batch effect.
4
Oscillation
Rapid up-down swings — the process is unstable, often from over-adjustment.
5
Mixture
Points avoiding the centre line — often two different processes combined.
6
No pattern
Random scatter around the median — stable, common-cause variation only.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
150

## Slide 151
ANALYZE · ROOT CAUSE
What is a root cause?
The deepest cause in the chain that you can actually act on — remove it, and the problem does not come back.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
151

## Slide 152
WHY EVIDENCE MATTERS
Fixing the wrong cause wastes the whole project.
If the analysis stops at the first plausible explanation, the team implements a change, the metric does not move, and confidence in the method is lost.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
152

## Slide 153
ANALYZE · 5 WHYS
The 5 Whys Technique
1
Start with the problem
State the effect precisely, using the data you measured.
2
Ask why — and answer with evidence
Each answer must be something you can point to, not a guess.
3
Repeat about five times
Five is a guide, not a rule — stop when you reach an actionable cause.
4
Watch for blame
If an answer names a person rather than a process, ask why again.
5
Stop at actionable
The root cause must be something within the team's power to change.
6
Verify with data
Test the final cause against the evidence before acting on it.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
153

## Slide 154
ANALYZE · 5 WHYS IN ACTION
5 Whys — Worked Example: Ticket Assignment Delay
1
PROBLEM: Tickets take 9.4 hours to assign vs a 4-hour target
▶
2
WHY? Tickets wait in the triage queue
▶
3
WHY? Only one agent triages, and only in the morning
▶
4
WHY? Triage is not in anyone's core role definition
▶
5
ROOT CAUSE: Triage ownership was never assigned when the process changed
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
154

## Slide 155
ANALYZE · CAUSE AND EFFECT · THE 5Ms
Fishbone (Ishikawa) — Ticket Assignment Is Delayed
Ticket
assignment
is delayed
Manpower
• One triage agent only
• No cover at peak
• Unclear ownership
Machine
• Ticket tool slow
• No auto-assignment
• Four systems to check
Measurement
• No SLA clock on triage
• Assignment time not tracked
• No baseline agreed
Method
• Triage rules ambiguous
• No priority definition
• Manual routing
Material
• Incomplete ticket info
• Wrong category chosen
• No template
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
155

## Slide 156
ANALYZE · FISHBONE METHOD
Building a Fishbone Diagram
1
Write the effect
Put the measured problem in the head of the fish — be specific.
2
Choose the categories
5M: Manpower, Method, Machine, Material, Measurement. Service teams often use 4P.
3
Brainstorm into each bone
Generate freely — no evaluation or debate during generation.
4
Go three levels deep
Ask 'why does that happen?' on each cause to reach the real driver.
5
Shortlist with multi-voting
Each team member votes; the causes with most votes go forward.
6
Verify with data
A cause on the diagram is a HYPOTHESIS until the data supports it.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
156

## Slide 157
ANALYZE · BRAINSTORMING
Brainstorming — Getting Good Causes Out
1
Quantity first
Generate a long list before evaluating anything.
2
No criticism
Judging ideas during generation stops people contributing.
3
Build on ideas
One person's half-idea is often another's breakthrough.
4
Everyone contributes
Use round-robin or brainwriting so the loudest voice does not dominate.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
157

## Slide 158
ANALYZE · MULTI-VOTING
Multi-Voting — Narrowing the List
1
Why use it
A long cause list needs to become a short, agreed shortlist.
2
How it works
Each member gets N votes (about a third of the number of items).
3
Vote independently
Vote privately first so nobody anchors on the manager's choice.
4
Then verify
The top-voted causes still have to be tested against the data.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
158

## Slide 159
YOUR ONLINE TOOLKIT · USED ACROSS DMAIC
Your Complete Online Toolkit
1
SIPOC & Process Map
Define — guided SIPOC, swimlane and handoffs — alfredang.github.io/sipoc/
2
5 Whys
Analyze — build and share the 5 Whys chain — alfredang.github.io/5whys/
3
Fishbone Diagram
Analyze — Ishikawa cause-and-effect builder — alfredang.github.io/fishbone/
4
Pareto Chart (collaborative)
Analyze — your team brainstorms and votes in one live session; the chart builds itself — alfredang.github.io/paretochart/
5
NovaSPC
Measure & Control — run charts, SPC charts and process capability from your CSV — alfredang.github.io/novaspc/
6
All free
No install, no sign-up. Everything stays in your browser.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
159

## Slide 160
ANALYZE · TEAM ROOT CAUSE SESSION
Using the Collaborative Pareto Tool in Your Team
1
Facilitator creates a session and shares the access code
▶
2
Every team member joins with the code
▶
3
The team brainstorms candidate causes into the session
▶
4
Each member votes on the causes that matter most
▶
5
The live Pareto chart reveals the vital few
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
160

## Slide 161
WHAT YOU'LL DO
Hands-On Labs — Analyze
1
Lab 7 — Pareto, Run Charts, Variation, Yield, DPU, and
A Pareto chart, a run chart and calculated yield, DPU, DPO, DPMO and s
2
Lab 8 — Root Cause Analysis with 5 Whys, Fishbone, and
A completed 5 Whys chain, a Fishbone diagram and an evidence-tested ca
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
161

## Slide 162
DMAIC · ANALYZE · HANDS-ON
Pareto, Run Charts, Variation, Yield, DPU, and DPMO
LAB 7
Turn collected data into decisions. Apply the Pareto principle to find the vital few categories, use a run chart to see behaviour over time, and calculate the standard Six Sigma process metrics.
You'll build
A Pareto chart, a run chart and calculated yield, DPU, DPO, DPMO and sigma level.
Tools & techniques: Pareto Chart tool (collaborative), NovaSPC, yield/DPU/DPO/DPMO, sigma level, variation
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
162

## Slide 163
LAB 7 · Pareto, Run Charts, Variation, Yield,
Pareto, Run Charts, Variation, Yield, DPU, and DPMO
1
STEP 1 OF 8
Build the Pareto table: category, count, percentage and cumulative percentage.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
163

## Slide 164
LAB 7 · Pareto, Run Charts, Variation, Yield,
Pareto, Run Charts, Variation, Yield, DPU, and DPMO
2
STEP 2 OF 8
In your group, open the collaborative Pareto tool — one member creates the session and shares the code, then everyone joins, brainstorms and votes to produce the live Pareto chart.
https://alfredang.github.io/paretochart/
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
164

## Slide 165
LAB 7 · Pareto, Run Charts, Variation, Yield,
Pareto, Run Charts, Variation, Yield, DPU, and DPMO
3
STEP 3 OF 8
Identify the vital few categories driving about 80% of the problem.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
165

## Slide 166
LAB 7 · Pareto, Run Charts, Variation, Yield,
Pareto, Run Charts, Variation, Yield, DPU, and DPMO
4
STEP 4 OF 8
Export your assignment-time data as CSV and plot a run chart in NovaSPC.
https://alfredang.github.io/novaspc/
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
166

## Slide 167
LAB 7 · Pareto, Run Charts, Variation, Yield,
Pareto, Run Charts, Variation, Yield, DPU, and DPMO
5
STEP 5 OF 8
Interpret the run chart for trend, shift, cluster and oscillation patterns.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
167

## Slide 168
LAB 7 · Pareto, Run Charts, Variation, Yield,
Pareto, Run Charts, Variation, Yield, DPU, and DPMO
6
STEP 6 OF 8
Calculate yield, DPU, DPO and DPMO from your defect data.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
168

## Slide 169
LAB 7 · Pareto, Run Charts, Variation, Yield,
Pareto, Run Charts, Variation, Yield, DPU, and DPMO
7
STEP 7 OF 8
Convert DPMO to a sigma level and interpret what it says about the process.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
169

## Slide 170
LAB 7 · Pareto, Run Charts, Variation, Yield,
Pareto, Run Charts, Variation, Yield, DPU, and DPMO
8
STEP 8 OF 8
Distinguish common-cause from special-cause variation and why the response differs.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
170

## Slide 171
LAB 7 · VERIFY
Pareto, Run Charts, Variation, Yield, DPU, and DPMO
✅ Check your work
Your cumulative percentage column reaches 100%, and you can state the sigma level with the DPMO it came from.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
171

## Slide 172
DMAIC · ANALYZE · HANDS-ON
Root Cause Analysis with 5 Whys, Fishbone, and Evidence
LAB 8
Move from symptom to cause. Apply the 5 Whys to drill past the obvious, organise candidate causes on a Fishbone diagram, then test each candidate against the evidence you actually collected.
You'll build
A completed 5 Whys chain, a Fishbone diagram and an evidence-tested cause shortlist.
Tools & techniques: 5 Whys tool, Fishbone tool, 5M categories, brainstorming, multi-voting
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
172

## Slide 173
LAB 8 · Root Cause Analysis with 5 Whys, Fishb
Root Cause Analysis with 5 Whys, Fishbone, and Evidence
1
STEP 1 OF 7
Write the problem statement precisely — the effect you are explaining.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
173

## Slide 174
LAB 8 · Root Cause Analysis with 5 Whys, Fishb
Root Cause Analysis with 5 Whys, Fishbone, and Evidence
2
STEP 2 OF 7
Complete a 5 Whys chain with the online 5 Whys tool, continuing until you reach an actionable cause.
https://alfredang.github.io/5whys/
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
174

## Slide 175
LAB 8 · Root Cause Analysis with 5 Whys, Fishb
Root Cause Analysis with 5 Whys, Fishbone, and Evidence
3
STEP 3 OF 7
Build a Fishbone diagram with the online Fishbone tool using the 5M categories: Manpower, Method, Machine, Material, Measurement.
https://alfredang.github.io/fishbone/
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
175

## Slide 176
LAB 8 · Root Cause Analysis with 5 Whys, Fishb
Root Cause Analysis with 5 Whys, Fishbone, and Evidence
4
STEP 4 OF 7
Brainstorm candidate causes into each category — no evaluation during generation.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
176

## Slide 177
LAB 8 · Root Cause Analysis with 5 Whys, Fishb
Root Cause Analysis with 5 Whys, Fishbone, and Evidence
5
STEP 5 OF 7
Use multi-voting to shortlist the most likely causes as a team.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
177

## Slide 178
LAB 8 · Root Cause Analysis with 5 Whys, Fishb
Root Cause Analysis with 5 Whys, Fishbone, and Evidence
6
STEP 6 OF 7
Test each shortlisted cause against your Lab 7 data — does the evidence support it?
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
178

## Slide 179
LAB 8 · Root Cause Analysis with 5 Whys, Fishb
Root Cause Analysis with 5 Whys, Fishbone, and Evidence
7
STEP 7 OF 7
State why the team must not jump straight to solutions.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
179

## Slide 180
LAB 8 · VERIFY
Root Cause Analysis with 5 Whys, Fishbone, and Evidence
✅ Check your work
Each shortlisted root cause is supported by named evidence, and your 5 Whys chain ends at something you can act on.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
180

## Slide 181
PHASE RECAP
Recap — Analyze
• Variation — Common cause is built into the process; special cause is an external, assignable signal.
• Pareto analysis — The 80/20 rule separates the vital few causes from the trivial many.
• Run charts — Plot the metric over time to reveal trend, shift, cluster and oscillation.
• 5 Whys — Ask why repeatedly to drill from the symptom down to an actionable cause.
• Fishbone diagram — Organise candidate causes by category — Manpower, Method, Machine, Material, Measurement.
• Evidence testing — A cause is only a root cause when the data you collected supports it.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
181

## Slide 182
DMAIC · IMPROVE
Improve — Fix the Cause
Countermeasures · 5S · Poka-Yoke · Standard work · Kaizen · Solution selection · Piloting
I
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
182

## Slide 183
IMPROVE · 10% OF THE COURSE
Key Concepts — Improve
1
Generating solutions
Brainstorm widely against the proven root cause before evaluating anything.
2
Solution selection
Score candidate solutions against weighted criteria before committing.
3
5S
Sort, Set in order, Shine, Standardise, Sustain — for physical and digital work.
4
Poka-Yoke
Mistake proofing makes the error difficult or impossible to make in the first place.
5
Standard work
Document the improved method so anyone can repeat it the same way.
6
Piloting
Test the change at small scale to expose issues before full rollout.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
183

## Slide 184
DMAIC · I — IMPROVE
Improve — What change will actually fix it?
The Improve phase generates, selects and pilots solutions that address the proven root cause.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
184

## Slide 185
IMPROVE · ROADMAP
Steps in the Improve Phase
1
Generate candidate solutions against the root cause
▶
2
Select using weighted criteria
▶
3
Pilot the change at small scale
▶
4
Measure whether the metric actually moved
▶
5
Standardise the new method
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
185

## Slide 186
IMPROVE · IDEA GENERATION
Generating Solutions
1
Brainstorming
Free generation against the specific root cause — not the general problem.
2
Brainwriting
Written idea generation; avoids the loudest voice dominating the room.
3
Benchmarking
Find who already does this well, internally or externally, and learn from them.
4
Anti-brainstorming
Ask how to make the problem worse, then invert every answer.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
186

## Slide 187
IMPROVE · PRIORITISATION
Prioritising Countermeasures — Impact vs Effort
Quick wins
High impact, low effort. Do these first — they build momentum and credibility.
Major projects
High impact, high effort. Worth doing, but plan and resource them properly.
Fill-ins
Low impact, low effort. Do them if there is spare capacity.
Thankless tasks
Low impact, high effort. Avoid these entirely.
EFFORT REQUIRED →
IMPACT →
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
187

## Slide 188
IMPROVE · CHOOSING OBJECTIVELY
The Solution Selection Matrix
1
List the criteria
Effectiveness, cost, time to implement, risk, ease of adoption.
2
Weight each criterion
Not all criteria matter equally — agree the weights first.
3
Score each solution
Score every candidate against each criterion on a consistent scale.
4
Rank by weighted total
Multiply score by weight, sum, and rank — the decision becomes defensible.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
188

## Slide 189
IMPROVE · 5S
5S — Organising the Workplace
1
SORT — remove what is not needed
▶
2
SET IN ORDER — a place for everything
▶
3
SHINE — clean and inspect regularly
▶
4
STANDARDISE — make the first 3S the norm
▶
5
SUSTAIN — audit and keep the discipline
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
189

## Slide 190
IMPROVE · 5S IN A SERVICE TEAM
5S Applied to Digital Work
1
Sort
Archive the ticket queues, folders and dashboards nobody uses.
2
Set in order
One agreed place for templates, runbooks and knowledge articles.
3
Shine
Regularly review and retire out-of-date knowledge base entries.
4
Standardise
Agreed naming conventions and ticket templates for everyone.
5
Sustain
A short monthly review to check the standard is still being followed.
6
Why it works
Less searching, fewer mistakes, faster onboarding for new agents.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
190

## Slide 191
IMPROVE · POKA-YOKE
Poka-Yoke — mistake proofing
Design the process so the error is difficult or impossible to make — rather than relying on people to be careful.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
191

## Slide 192
IMPROVE · POKA-YOKE LEVELS
Three Levels of Mistake Proofing
Prevention
The error cannot happen
• Strongest form — design it out.
• A required field blocks submission.
• A connector only fits one way.
Detection
The error is caught immediately
• The error happens but is flagged at once.
• Validation warns on an invalid category.
• Weaker, but often easier to add.
Mitigation
The impact is reduced
• The error happens and is not caught.
• But its consequence is limited.
• Weakest — use only when the others cannot apply.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
192

## Slide 193
IMPROVE · STANDARD WORK
Standard Work
1
What it is
The documented, current best-known way to perform the task.
2
Why it matters
You cannot improve a process that everyone performs differently.
3
What it contains
The sequence, the time each step takes and the quality checks.
4
Who writes it
The people who do the work — not a manager writing in isolation.
5
Keep it living
Update it every time a better method is proven.
6
The Lean insight
Standard work is the baseline for the NEXT improvement, not a straitjacket.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
193

## Slide 194
IMPROVE · KAIZEN
Kaizen — Continuous Small Improvement
1
The principle
Many small improvements beat waiting for one perfect large one.
2
Who does it
Everyone — Kaizen is explicitly not reserved for specialists.
3
Kaizen event
A focused 3-5 day workshop to fix one process end to end.
4
Yellow Belt fit
This is exactly the scale of improvement a Yellow Belt leads.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
194

## Slide 195
IMPROVE · PILOTING
Piloting Before Full Rollout
1
Why pilot
Exposes practical issues cheaply, before they affect every customer.
2
Keep it small
One team, one shift or one ticket category is usually enough.
3
Measure the same way
Use the identical operational definition as your baseline, or you cannot compare.
4
Run it long enough
Cover a full business cycle so you see normal variation.
5
Decide honestly
Adopt, adapt or abandon — a failed pilot that saves a bad rollout is a success.
6
Then standardise
Only after the pilot proves the gain do you write it into standard work.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
195

## Slide 196
WHAT YOU'LL DO
Hands-On Labs — Improve
1
Lab 9 — Countermeasures, 5S, Mistake Proofing, Standar
A prioritised countermeasure set with a 5S plan, a poka-yoke design an
2
Lab 13 (elective) — Solution Selection Matrix, Benchmarking,
A scored solution selection matrix, a benchmarking summary and an FMEA
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
196

## Slide 197
DMAIC · IMPROVE · HANDS-ON
Countermeasures, 5S, Mistake Proofing, Standard Work, and Kaizen
LAB 9
Generate and select countermeasures that attack the root cause you proved — not the symptom. Apply the core Lean improvement tools: 5S, poka-yoke, visual management, standard work and Kaizen.
You'll build
A prioritised countermeasure set with a 5S plan, a poka-yoke design and standard work.
Tools & techniques: Brainstorming, 5S, poka-yoke, visual management, standard work, Kaizen
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
197

## Slide 198
LAB 9 · Countermeasures, 5S, Mistake Proofing,
Countermeasures, 5S, Mistake Proofing, Standard Work, and Kaizen
1
STEP 1 OF 7
Generate countermeasures for each proven root cause — quantity before quality.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
198

## Slide 199
LAB 9 · Countermeasures, 5S, Mistake Proofing,
Countermeasures, 5S, Mistake Proofing, Standard Work, and Kaizen
2
STEP 2 OF 7
Prioritise using an impact vs effort matrix to find the quick wins.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
199

## Slide 200
LAB 9 · Countermeasures, 5S, Mistake Proofing,
Countermeasures, 5S, Mistake Proofing, Standard Work, and Kaizen
3
STEP 3 OF 7
Apply 5S thinking — Sort, Set in order, Shine, Standardise, Sustain — including to digital work.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
200

## Slide 201
LAB 9 · Countermeasures, 5S, Mistake Proofing,
Countermeasures, 5S, Mistake Proofing, Standard Work, and Kaizen
4
STEP 4 OF 7
Design one poka-yoke that makes the error difficult or impossible to make.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
201

## Slide 202
LAB 9 · Countermeasures, 5S, Mistake Proofing,
Countermeasures, 5S, Mistake Proofing, Standard Work, and Kaizen
5
STEP 5 OF 7
Draft standard work so the improved method is repeatable by anyone.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
202

## Slide 203
LAB 9 · Countermeasures, 5S, Mistake Proofing,
Countermeasures, 5S, Mistake Proofing, Standard Work, and Kaizen
6
STEP 6 OF 7
Plan a Kaizen event or pilot to test the countermeasure at small scale first.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
203

## Slide 204
LAB 9 · Countermeasures, 5S, Mistake Proofing,
Countermeasures, 5S, Mistake Proofing, Standard Work, and Kaizen
7
STEP 7 OF 7
Distinguish a containment countermeasure from a permanent solution.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
204

## Slide 205
LAB 9 · VERIFY
Countermeasures, 5S, Mistake Proofing, Standard Work, and Kaizen
✅ Check your work
Every countermeasure traces back to a proven root cause, and your poka-yoke prevents rather than detects the error.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
205

## Slide 206
DMAIC · IMPROVE · HANDS-ON
Elective — Solution Selection Matrix, Benchmarking, and FMEA
LAB 13
ELECTIVE
Three Improve-phase tools from the original course. Score solutions against weighted criteria, benchmark against outstanding practice, and use FMEA to find how a proposed change could fail before it does.
You'll build
A scored solution selection matrix, a benchmarking summary and an FMEA with RPN.
Tools & techniques: Solution selection matrix, benchmarking, FMEA, RPN scoring
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
206

## Slide 207
LAB 13 · Elective — Solution Selection Matrix,
Elective — Solution Selection Matrix, Benchmarking, and FMEA
1
STEP 1 OF 5
Agree the selection criteria and weight each by importance.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
207

## Slide 208
LAB 13 · Elective — Solution Selection Matrix,
Elective — Solution Selection Matrix, Benchmarking, and FMEA
2
STEP 2 OF 5
Score every candidate solution against the weighted criteria and rank the results.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
208

## Slide 209
LAB 13 · Elective — Solution Selection Matrix,
Elective — Solution Selection Matrix, Benchmarking, and FMEA
3
STEP 3 OF 5
Benchmark your process against an internal or external reference and note the gap.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
209

## Slide 210
LAB 13 · Elective — Solution Selection Matrix,
Elective — Solution Selection Matrix, Benchmarking, and FMEA
4
STEP 4 OF 5
Build an FMEA: failure mode, effect, cause, then score Severity, Occurrence and Detection.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
210

## Slide 211
LAB 13 · Elective — Solution Selection Matrix,
Elective — Solution Selection Matrix, Benchmarking, and FMEA
5
STEP 5 OF 5
Calculate RPN = S x O x D and address the highest-RPN failure modes first.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
211

## Slide 212
LAB 13 · VERIFY
Elective — Solution Selection Matrix, Benchmarking, and FMEA
✅ Check your work
Your matrix ranks solutions by weighted score, and every FMEA row has an RPN and an action for the highest scores.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
212

## Slide 213
PHASE RECAP
Recap — Improve
• Generating solutions — Brainstorm widely against the proven root cause before evaluating anything.
• Solution selection — Score candidate solutions against weighted criteria before committing.
• 5S — Sort, Set in order, Shine, Standardise, Sustain — for physical and digital work.
• Poka-Yoke — Mistake proofing makes the error difficult or impossible to make in the first place.
• Standard work — Document the improved method so anyone can repeat it the same way.
• Piloting — Test the change at small scale to expose issues before full rollout.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
213

## Slide 214
DMAIC · CONTROL
Control — Hold the Gain
Control plan · Visual management · SOPs · Huddles · A3 · Handover · Certification
C
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
214

## Slide 215
CONTROL · 5% OF THE COURSE
Key Concepts — Control
1
Control plan
Metric, target, monitoring method, frequency, owner and reaction plan.
2
Process control
A process is in control when it varies consistently within expected limits.
3
Visual management
Boards and dashboards keep the improved performance visible to everyone.
4
Standard operating procedures
Written instructions that lock in the improved method.
5
Team huddles
Short, regular stand-ups that surface problems while they are still small.
6
A3 and handover
One-page storytelling to summarise, hand over and sustain the improvement.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
215

## Slide 216
DMAIC · C — CONTROL
Control — How do we make the gain stick?
Without the Control phase, processes drift back to the old way within months and the whole project is wasted.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
216

## Slide 217
CONTROL · ROADMAP
Steps in the Control Phase
1
Build the control plan
▶
2
Set up monitoring and visual management
▶
3
Document the SOP and standard work
▶
4
Hand over to the process owner
▶
5
Close the project and share the learning
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
217

## Slide 218
CONTROL · THE CONTROL PLAN
The Control Plan — Six Required Columns
1
Metric
What is being monitored — the same operational definition as the baseline.
2
Target
The agreed acceptable value or range.
3
Method
How the measurement is taken — report, dashboard, sample or audit.
4
Frequency
How often it is checked: per shift, daily, weekly.
5
Owner
The named person accountable — a role, never 'the team'.
6
Reaction plan
Exactly what happens when the metric falls outside target.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
218

## Slide 219
CONTROL · ACCOUNTABILITY
A control plan without a named owner is a wish.
Every row needs a person accountable and a specific action to take when the number goes wrong — otherwise nothing happens.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
219

## Slide 220
CONTROL · PROCESS CONTROL
What is process control?
A process is 'in control' when it varies consistently within expected limits over time — predictable, even if not yet perfect.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
220

## Slide 221
CONTROL · A CRITICAL DISTINCTION
Control Limits vs Specification Limits
Set by the customer
Set by the process
• Specification limits (LSL / USL)
– Given by the CUSTOMER
– Define what counts as a defect
– Do not change when the process changes
– Outside them = a defect
• Control limits (LCL / UCL)
– Calculated from the PROCESS itself
– Typically the mean ± 3 standard deviations
– Change when the process changes
– Outside them = a special cause to investigate
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
221

## Slide 222
CONTROL · SPC AWARENESS
Statistical Process Control (SPC)
1
What it is
Monitoring a process over time so problems are predicted, not discovered late.
2
The core idea
Plot the metric against control limits and watch for non-random patterns.
3
Why it saves money
Preventing defects always costs less than inspecting and reworking them.
4
Yellow Belt level
You are expected to read and interpret a control chart, not to construct one.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
222

## Slide 223
CONTROL · MAKING IT VISIBLE
Visual Management
1
Visual boards
Display the metric, the target and the current status where the team works.
2
Make it obvious
Anyone should see whether performance is on target within a few seconds.
3
Team huddles
A short daily stand-up at the board — 15 minutes maximum.
4
Drives ownership
When performance is visible, the team owns it rather than the manager.
5
Surfaces issues early
Problems are raised while they are still small and cheap to fix.
6
Keep it current
An out-of-date board is worse than no board — it teaches people to ignore it.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
223

## Slide 224
CONTROL · SOPs
Standard Operating Procedures (SOPs)
1
Written instructions
Describe how to perform the task to achieve the required result.
2
Include the measures
State the benchmarks and quality checks, not only the steps.
3
Centrally accessible
Held in one agreed place everyone can reach and search.
4
Version controlled
It must be obvious which version is current.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
224

## Slide 225
CONTROL · GO GEMBA
Go to the Gemba
1
Gemba means 'the real place'
Where the work actually happens — not the meeting room.
2
Go and see
Observe the process directly rather than relying on reports about it.
3
Ask, do not blame
The purpose is to understand the process, never to audit the person.
4
Why it works
Reports show what was recorded; Gemba shows what actually happens.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
225

## Slide 226
CONTROL · THE A3 REPORT
The A3 — One Page That Tells the Whole Story
1
Background
Why this problem was worth working on.
2
Current state
The baseline, with the data and process map.
3
Goal
The target condition, stated as a measurable number.
4
Root cause analysis
What the 5 Whys and Fishbone actually proved.
5
Countermeasures
What was changed, and why that addresses the proven cause.
6
Results & follow-up
Whether the metric moved, and who now owns the control plan.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
226

## Slide 227
CONTROL · CLOSING THE PROJECT
Project Handover and Closure
1
Confirm the improvement held for a full cycle
▶
2
Hand the control plan to the named process owner
▶
3
Train everyone on the new standard work
▶
4
Document the financial or service benefit
▶
5
Share the learning so others can reuse it
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
227

## Slide 228
WHAT YOU'LL DO
Hands-On Labs — Control
1
Lab 10 — Control Plan, A3 Summary, Handover, and Certif
A control plan, an A3 one-page summary, a handover checklist and a rea
2
Lab 14 (elective) — Descriptive Statistics and Implementatio
A descriptive statistics summary and a dated implementation plan.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
228

## Slide 229
DMAIC · CONTROL · HANDS-ON
Control Plan, A3 Summary, Handover, and Certification Readiness
LAB 10
Hold the gain. Build a control plan that names the metric, the target, the monitoring frequency, the owner and the reaction plan — then tell the whole improvement story on a single A3 page and hand it over.
You'll build
A control plan, an A3 one-page summary, a handover checklist and a readiness plan.
Tools & techniques: Control plan, SPC thinking, visual management, A3 report, handover
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
229

## Slide 230
LAB 10 · Control Plan, A3 Summary, Handover, an
Control Plan, A3 Summary, Handover, and Certification Readiness
1
STEP 1 OF 6
Create the control plan: metric, target, monitoring method, frequency, owner, reaction plan.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
230

## Slide 231
LAB 10 · Control Plan, A3 Summary, Handover, an
Control Plan, A3 Summary, Handover, and Certification Readiness
2
STEP 2 OF 6
Define the visual management approach — board, dashboard or huddle — that keeps it visible.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
231

## Slide 232
LAB 10 · Control Plan, A3 Summary, Handover, an
Control Plan, A3 Summary, Handover, and Certification Readiness
3
STEP 3 OF 6
Specify the reaction plan: exactly what happens when a metric falls outside target.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
232

## Slide 233
LAB 10 · Control Plan, A3 Summary, Handover, an
Control Plan, A3 Summary, Handover, and Certification Readiness
4
STEP 4 OF 6
Write the A3 summary: background, current state, goal, analysis, countermeasures, results, follow-up.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
233

## Slide 234
LAB 10 · Control Plan, A3 Summary, Handover, an
Control Plan, A3 Summary, Handover, and Certification Readiness
5
STEP 5 OF 6
Prepare the handover checklist so the process owner can sustain it without you.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
234

## Slide 235
LAB 10 · Control Plan, A3 Summary, Handover, an
Control Plan, A3 Summary, Handover, and Certification Readiness
6
STEP 6 OF 6
Complete your personal certification readiness plan — which topics need most review.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
235

## Slide 236
LAB 10 · VERIFY
Control Plan, A3 Summary, Handover, and Certification Readiness
✅ Check your work
Every control plan row has a named owner and a reaction plan, and your A3 fits on one page.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
236

## Slide 237
DMAIC · CONTROL · HANDS-ON
Elective — Descriptive Statistics and Implementation Planning
LAB 14
ELECTIVE
Close the loop. Compute the measures of central tendency and dispersion that describe your data, then convert the selected countermeasures into a dated implementation plan with owners and barriers identified.
You'll build
A descriptive statistics summary and a dated implementation plan.
Tools & techniques: Mean, median, range, standard deviation, implementation planning
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
237

## Slide 238
LAB 14 · Elective — Descriptive Statistics and
Elective — Descriptive Statistics and Implementation Planning
1
STEP 1 OF 4
Compute the mean and median for your assignment-time data and compare them.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
238

## Slide 239
LAB 14 · Elective — Descriptive Statistics and
Elective — Descriptive Statistics and Implementation Planning
2
STEP 2 OF 4
Compute the range and standard deviation to describe the spread.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
239

## Slide 240
LAB 14 · Elective — Descriptive Statistics and
Elective — Descriptive Statistics and Implementation Planning
3
STEP 3 OF 4
Explain what the mean-versus-median difference reveals about outliers and skew.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
240

## Slide 241
LAB 14 · Elective — Descriptive Statistics and
Elective — Descriptive Statistics and Implementation Planning
4
STEP 4 OF 4
Write the implementation plan: action, owner, date, barriers and mitigation.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
241

## Slide 242
LAB 14 · VERIFY
Elective — Descriptive Statistics and Implementation Planning
✅ Check your work
You can explain why the mean and median differ in your data, and every implementation action has an owner and a date.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
242

## Slide 243
PHASE RECAP
Recap — Control
• Control plan — Metric, target, monitoring method, frequency, owner and reaction plan.
• Process control — A process is in control when it varies consistently within expected limits.
• Visual management — Boards and dashboards keep the improved performance visible to everyone.
• Standard operating procedures — Written instructions that lock in the improved method.
• Team huddles — Short, regular stand-ups that surface problems while they are still small.
• A3 and handover — One-page storytelling to summarise, hand over and sustain the improvement.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
243

## Slide 244
WRAP-UP
Course Summary & Next Steps
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
244

## Slide 245
YOUR IMPROVEMENT PACKAGE
What You Achieved — The Full DMAIC Journey
D
Define
• Captured VOC and CTQ
• Wrote the charter
• Built the SIPOC
• Mapped the process
M
Measure
• Found the 8 wastes
• Built the data plan
• Collected the baseline
• Calculated DPMO
A
Analyze
• Built the Pareto
• Read the run chart
• Ran 5 Whys and Fishbone
• Proved the cause
I
Improve
• Selected solutions
• Applied 5S and poka-yoke
• Wrote standard work
• Piloted the change
C
Control
• Built the control plan
• Set visual management
• Wrote the A3
• Handed over
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
245

## Slide 246
WHAT YOU BUILT
Your Integrated Improvement Package
1
Role and scenario
Yellow Belt responsibility table and a selected improvement scenario.
2
VOC, CTQ and waste
Customer requirements translated to CTQs, plus a waste walk log.
3
SIPOC and process map
Macro and detailed maps with pain points and handoffs marked.
4
Charter and Define pack
PDCA charter, problem statement, scope and stakeholder map.
5
Measurement and analysis
Data collection plan, check sheet, Pareto, run chart and metrics.
6
Root cause and countermeasures
5 Whys, Fishbone, evidence tests and prioritised countermeasures.
7
Control plan and A3
Control plan, visual management approach, A3 summary and handover.
8
Certification readiness
Your personal review plan for the assessment.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
246

## Slide 247
BEFORE THE ASSESSMENT
Final Readiness Checklist
1
Can you explain the Yellow Belt role and where it stops?
2
Can you define Lean, Six Sigma and Lean Six Sigma in your own words?
3
Can you trace a VOC statement through to a CTQ and a metric?
4
Can you name the eight wastes and give a service example of each?
5
Can you explain each DMAIC phase and what it delivers?
6
Can you calculate yield, DPU, DPO and DPMO from raw data?
7
Can you interpret a Pareto chart and a run chart?
8
Can you explain your root cause with the evidence behind it?
9
Can you describe how the control plan sustains the gain?
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
247

## Slide 248
NEXT STEPS
Continuing Your Lean Six Sigma Journey
1
Apply it at work
Run one small PDCA improvement in your own area within 30 days.
2
Green Belt
The next step — leads smaller DMAIC projects and handles the statistics.
3
Keep the templates
Your lab outputs are reusable templates for real projects.
4
Join the community
Share improvements with colleagues; Kaizen spreads by example.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
248

## Slide 249
ASSESSMENT
Final Assessment
Written Assessment (SAQ, 60 minutes) followed by the Case Study (90 minutes). Both are open book.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
249

## Slide 250
ON ASSESSMENT DAY
Assessment Flow
1
TRAQOM survey — scan the QR code on the LMS
▶
2
Assessment digital attendance — scan the SSG QR
▶
3
Sit the WA (SAQ), then the Case Study — open book
▶
4
Submit your answers on the LMS
▶
5
Sign the Assessment Summary Record
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
250

## Slide 251
TRAQOM · SSG DIGITAL ATTENDANCE
Digital Attendance (Assessment)
1
Trainer displays the SSG digital attendance QR code
▶
2
Scan the QR code with your phone camera
▶
3
Key in your NRIC/FIN and submit
▶
4
Attendance must be recorded before you begin the papers
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
251

## Slide 252
YOUR FEEDBACK
TRAQOM Survey
1
Open the TRAQOM survey link on the LMS
▶
2
Key in the last four characters of your NRIC/FIN
▶
3
Key in the six-digit course run ID
▶
4
Complete and submit — your feedback shapes this course
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
252

## Slide 253
AFTER THE COURSE
Certificate & Support
• Two e-certificates are awarded on demonstrating competency and achieving at least 75% attendance.
• A SkillsFuture Statement of Attainment (SOA) is issued for the WSQ assessment.
• Email: enquiry@tertiaryinfotech.com
• Tel / WhatsApp: +65 6100 0613
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
253

## Slide 254
END OF COURSE
Thank You!
Go and improve one process this month — that is what a Yellow Belt is for.
Certified Lean Six Sigma Yellow Belt (CLSSYB) Training · TGS-2025053922
© 2026 Tertiary Infotech Academy Pte Ltd
254